## Slide 1: A Study of Remining Practices within the Cambria District
Mike Haney, PG
Rock Martin, PG
Mike Schirato, PG
Greg Shuler, PG
PADEP Cambria District Mining Office

## Slide 2: Cambria District Mining: Remining Review
Objectives: To review data from remining sites within the Cambria District to identify trends
  Expand geographical and statistical coverage of previous research
  Refine the categorical analysis by sorting results
    County
    Watershed
    Coal Seam
Identify specific topics for further study
Illustrate practical application of conclusions

## Slide 3: Pennsylvania Bituminous Remining: Previous Research
M.W. Smith, K.B.C. Brady, and J. W. Hawkins presented research from 1995 to 2002. (up to 233 discharges within 110 sites)
Statistical comparison of pollutional loading from pre-existing discharges on remined sites
Baseline vs. post-mining
Abatement techniques, etc.

## Slide 4: Pennsylvania Bituminous Remining: Previous Research
Results were derived from a comparison of pre- vs. post-mining analytical data that displayed a statistically significant median value change about a 95% confidence interval range.
This study uses the same qualifying criteria and overall analysis methodology
Refinement sorting and graphical illustration/mapping displays
Previous work defined and identified qualifying site data as:
Pre-existing pollutional discharge data wherein baseline loading values could be established and compared to post-mining datasets
A minimum of 12 time-series data points collected over a hydrologic year
Sorted by relevant mining parameter
Extra data could be used to assess remining methods/abatement techniques

## Slide 5
233 discharges within 110 sites. 6 sites within the Cambria Mining District

## Slide 6
101 discharges within 25 sites all within the Cambria Mining District

## Slide 7: Data Sourcing:
Digital tracking of surface mine permits with Pa Title 25 Chapter 87 Subchapter F protection.
Physical files of sites that qualified (mining complete, bond released)
  Module 26:Remining / Baseline calculations / coal seam info/ method
  Module 8 background data
Microfilm of archived sites
Qualification review: minimum 12 time-series dataset; corresponding post-mining dataset
Baseline calculation correction/update for statistical comparison

## Slide 8
Baseline calculation confidence interval correction:
This allowed for:
- Parameter by Parameter comparison for pre-existing, pre-mining discharge baseline data vs. post-mining monitoring data obtained prior to bond release.
- Compilation of data across the study area for geographical sorting

## Slide 9
Discharge Eliminated by Remining
Discharge Degraded by Remining
Discharge Improved by Remining
No Post Mining Change

## Slide 10
Discharge Eliminated by Remining
Discharge Degraded by Remining
Discharge Improved by Remining
No Post Mining Change

## Slide 11
Statistics by Discharge |  |  |  |  |  |  |  | 
100% | 101 | discharges | within | 25 | permits |  |  | 
26.73% | 27 | discharges eliminated by remining |  |  |  |  |  | 
16.83% | 18 | discharges degraded for at least one parameter |  |  |  |  |  | 
22.77% | 23 | discharges indicate loading reduction with no degradation |  |  |  |  |  | 
33.66% | 33 | discharges indicate no significant change for ay parameter |  |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change | 
Acidity | 73 | 4 | 5.48% | 16 | 21.92% | 53 | 72.60% | 
Iron | 73 | 10 | 13.70% | 12 | 16.44% | 51 | 69.86% | 
Manganese | 73 | 11 | 15.07% | 13 | 17.81% | 49 | 67.12% | 
Aluminum | 61 | 2 | 3.28% | 7 | 11.48% | 52 | 85.25% | 
Sulfates | 64 | 11 | 17.19% | 6 | 9.38% | 47 | 73.44% | 
Flow | 72 | 5 | 6.94% | 11 | 15.28% | 56 | 77.78% | 
Discharge Eliminated by Remining
Discharge Degraded by Remining
Discharge Improved by Remining
No Post Mining Change
Color coding scheme was applied to GIS graphics for each discharge location for reference

## Slide 13
Chart: 
| Eliminated | Degraded | Improved | No Change
Overall | 0.26733 | 0.16832 | 0.22772 | 0.33663
Chart: 
| Eliminated | Degraded | Improved | No Change
Somerset County | 0.30909 | 0.18182 | 0.16364 | 0.34545
Chart: 
| Eliminated | Degraded | Improved | No Change
Indiana County | 0.18182 | 0.22727 | 0.22727 | 0.36364
Chart: 
| Eliminated | Degraded | Improved | No Change
Cambria County | 0.25 | 0.125 | 0.33333 | 0.29167

## Slide 14
Chart: Degraded Discharges: Parameter Sorting
| Acidity | Iron | Manganese | Aluminum | Sulfates | Flow
% degraded | 0.054795 | 0.13699 | 0.15068 | 0.032787 | 0.17188 | 0.069444

## Slide 15
Overall Cambria District: Remining Review

## Slide 16
Chart: Degraded Discharges by County
| Cambria | Somerset | Indiana
Degraded | 3 | 10 | 5
55%
17%
28%

## Slide 17
Somerset Co. Remining Statistics |  |  |  |  |  |  | 
Statistics by Discharge |  |  |  |  |  |  | 
100% | 55 | discharges | within | 11 | permits |  | 
31% | 17 | discharges eliminated by remining |  |  |  |  | 
18.18% | 10 | discharges degraded for at least one parameter |  |  |  |  | 
16.36% | 9 | discharges indiacte loading reductionwith no degradation |  |  |  |  | 
35% | 19 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 38 | 1 | 2.63% | 6 | 15.79% | 31 | 81.58%
Iron | 38 | 7 | 18.42% | 2 | 5.26% | 29 | 76.32%
Manganese | 38 | 5 | 13.16% | 4 | 10.53% | 29 | 76.32%
Aluminum | 26 | 1 | 3.85% | 1 | 3.85% | 24 | 92.31%
Sulfates | 33 | 8 | 24.24% | 4 | 12.12% | 21 | 63.64%
Flow | 37 | 3 | 8.11% | 6 | 16.22% | 28 | 75.68%
Remining Review: Somerset County
SOMERSET

## Slide 18
Remining Review: Indiana County
Indiana Co. Remining Statistics |  |  |  |  |  |  | 
Statistics by Discharge |  |  |  |  |  |  | 
100% | 22 | discharges | within | 8 | permits |  | 
18% | 4 | discharges eliminated by remining |  |  |  |  | 
22.73% | 5 | discharges degraded for at least one parameter |  |  |  |  | 
22.73% | 5 | discharges indiacte loading reductionwith no degradation |  |  |  |  | 
36% | 8 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 18 | 1 | 5.56% | 4 | 22.22% | 13 | 72.22%
Iron | 18 | 2 | 11.11% | 5 | 27.78% | 11 | 61.11%
Manganese | 18 | 4 | 22.22% | 2 | 11.11% | 12 | 66.67%
Aluminum | 17 | 1 | 5.88% | 2 | 11.76% | 14 | 82.35%
Sulfates | 16 | 3 | 18.75% | 0 | 0.00% | 13 | 81.25%
Flow | 18 | 3 | 16.67% | 2 | 11.11% | 12 | 66.67%

## Slide 19
Remining Review: Cambria County
Cambria County Remining Statistics |  |  |  |  |  |  | 
Statistics by Discharge |  |  |  |  |  |  | 
100% | 24 | discharges | within | 6 | permits |  | 
25% | 6 | discharges eliminated by remining |  |  |  |  | 
12.50% | 3 | discharges degraded for at least one parameter |  |  |  |  | 
33.33% | 8 | discharges indiacte loading reductionwith no degradation |  |  |  |  | 
29% | 7 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 18 | 2 | 11.11% | 6 | 33.33% | 10 | 55.56%
Iron | 18 | 1 | 5.56% | 6 | 33.33% | 11 | 61.11%
Manganese | 18 | 2 | 11.11% | 7 | 38.89% | 9 | 50.00%
Aluminum | 18 | 0 | 0.00% | 4 | 22.22% | 14 | 77.78%
Sulfates | 16 | 1 | 6.25% | 2 | 12.50% | 13 | 81.25%
Flow | 18 | 0 | 0.00% | 3 | 16.67% | 15 | 83.33%

## Slide 20
Remining Review: Conemaugh Watershed
Conemaugh Watershed Remining Statistics |  |  |  |  |  |  | 
100% | 55 | discharges | within | 11 | permits |  | 
22% | 12 | discharges eliminated by remining |  |  |  |  | 
18.18% | 10 | discharges degraded for at least one parameter |  |  |  |  | 
20.00% | 11 | discharges indicate loading reduction for at least one parameter |  |  |  |  | 
40% | 22 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 43 | 1 | 2.33% | 9 | 20.93% | 33 | 76.74%
Iron | 43 | 5 | 11.63% | 8 | 18.60% | 30 | 69.77%
Manganese | 43 | 5 | 11.63% | 6 | 13.95% | 32 | 74.42%
Aluminum | 42 | 2 | 4.76% | 3 | 7.14% | 37 | 88.10%
Sulfates | 39 | 6 | 15.38% | 2 | 5.13% | 31 | 79.49%
Flow | 42 | 3 | 7.14% | 4 | 9.52% | 35 | 83.33%

## Slide 21
Remining Review: Kiskiminetas Watershed
Kiskiminetas Watershed Remining Statistics |  |  |  |  |  |  | 
100% | 4 | discharges | within | 3 | permits |  | 
50% | 2 | discharges eliminated by remining |  |  |  |  | 
25.00% | 1 | discharges degraded for at least one parameter |  |  |  |  | 
25.00% | 1 | discharges indicate loading reduction for at least one parameter |  |  |  |  | 
0% | 0 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 2 | 0 | 0.00% | 1 | 50.00% | 1 | 50.00%
Iron | 2 | 1 | 50.00% | 1 | 50.00% | 0 | 0.00%
Manganese | 2 | 1 | 50.00% | 0 | 0.00% | 1 | 50.00%
Aluminum | 1 | 0 | 0.00% | 1 | 100.00% | 0 | 0.00%
Sulfates | 1 | 0 | 0.00% | 0 | 0.00% | 1 | 100.00%
Flow | 1 | 0 | 0.00% | 1 | 100.00% | 0 | 0.00%

## Slide 22
Remining Review: Kiskiminetas-Conemaugh Watershed
Kiski-Conemaugh Watershed Remining Statistics |  |  |  |  |  |  | 
100% | 59 | discharges | within | 14 | permits |  | 
24% | 14 | discharges eliminated by remining |  |  |  |  | 
18.64% | 11 | discharges degraded for at least one parameter |  |  |  |  | 
20.34% | 12 | discharges indicate loading reduction for at least one parameter |  |  |  |  | 
37% | 22 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 45 | 1 | 2% | 10 | 22% | 34 | 76%
Iron | 45 | 6 | 13% | 9 | 20% | 30 | 67%
Manganese | 45 | 6 | 13% | 6 | 13% | 33 | 73%
Aluminum | 43 | 2 | 5% | 4 | 9% | 37 | 86%
Sulfates | 40 | 6 | 15% | 2 | 5% | 32 | 80%
Flow | 43 | 3 | 7% | 5 | 12% | 35 | 81%

## Slide 23
Remining Review: Youghiogheny-Casselman Watershed
Youghiogheny Watershed Remining Statistics |  |  |  |  |  |  | 
100% | 23 | discharges | within | 7 | permits |  | 
39% | 9 | discharges eliminated by remining |  |  |  |  | 
17.39% | 4 | discharges degraded for at least one parameter |  |  |  |  | 
21.74% | 5 | discharges indiacte loading reductionwith no degradation |  |  |  |  | 
22% | 5 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 14 | 1 | 7.14% | 4 | 28.57% | 9 | 64.29%
Iron | 14 | 1 | 7.14% | 0 | 0.00% | 13 | 92.86%
Manganese | 14 | 4 | 28.57% | 2 | 14.29% | 8 | 57.14%
Aluminum | 7 | 0 | 0.00% | 1 | 14.29% | 6 | 85.71%
Sulfates | 8 | 2 | 25.00% | 1 | 12.50% | 5 | 62.50%
Flow | 14 | 2 | 14.29% | 4 | 28.57% | 8 | 57.14%

## Slide 24
Remining Review: Upper West Branch Susquehanna Watershed
Upper West Branch Susquehanna Watershed Remining Statistics |  |  |  |  |  |  | 
100% | 14 | discharges | within | 2 | permits |  | 
21% | 3 | discharges eliminated by remining |  |  |  |  | 
14.29% | 2 | discharges degraded for at least one parameter |  |  |  |  | 
28.57% | 4 | discharges indiacte loading reductionwith no degradation |  |  |  |  | 
29% | 4 | discharges indicate no significant change for ay parameter |  |  |  |  | 
Statistics by Parameter for post-remining discharges |  |  |  |  |  |  | 
 | # points | # degraded | % degraded | # improved | % improved | # no change | % no change
Acidity | 11 | 2 | 18.18% | 1 | 9.09% | 8 | 72.73%
Iron | 11 | 1 | 9.09% | 2 | 18.18% | 8 | 72.73%
Manganese | 11 | 1 | 9.09% | 4 | 36.36% | 6 | 54.55%
Aluminum | 11 | 0 | 0.00% | 2 | 18.18% | 9 | 81.82%
Sulfates | 11 | 1 | 9.09% | 1 | 9.09% | 9 | 81.82%
Flow | 11 | 0 | 0.00% | 1 | 9.09% | 10 | 90.91%

## Slide 25
2017 Cambria District Remining Review:
Coal Seam Overall Statistics

## Slide 26
2017 Cambria District Remining Review:
Comparison to earlier PA DEP studies (Smith et. al 2002)

## Slide 27
2017 Cambria District Remining Review:
Comparison to earlier PA DEP studies (Smith et. al 2002)

## Slide 28: Ideas for Further Research
Itemize statistics based on remining abatement techniques, for example:
Extend the statistical compilation to individual parameters for each coal seam
Produce some publications that include our conclusions and recommendations
Combine our overall statistics (2017 review) with those of previous studies

## Slide 29: Thank You!
Rock Martin, PG
Technical Services Section Chief
Cambria District Mining Office
286 Industrial Park Rd
Ebensburg, PA 15931
martin@pa.gov